## Slide 1: Informational Public Meeting #2 City 4 Expansion, City 7 & 8 Basins October 29th, 2026
1

## Slide 2: Executive Background – City 4 Expansion, City 7 and 8 Basins
Previous City 4 Expansion Public Meeting held on May 15, 2025.
Previous City 7 and 8 Basins Public Meeting held on November 4, 2025.
Presented the proposed septic-to-sewer improvements and planning-level costs.
This second public meeting provides an update and opportunity for additional community feedback and discuss a path forward.

## Slide 3: Increased Risk: Florida Septic Systems
High water table provides less space/time for effluent to be filtered before it reaches the
groundwater.
Limestone bedrock is porous and does not facilitate natural attenuation efficiently.
3
Flooding can cause septic tanks to overflow into nearby storm drains or back into residential pipes.
Source: Miami Waterkeeper
Source: Miami Waterkeeper
Source: Miami Waterkeeper

## Slide 4: Septic Tank Vulnerability
Septic Tank systems can release contaminants which can then migrate through groundwater and impact nearby water bodies
Septic system performance depends on separation from groundwater
Minimum ~42 inches of separation is needed for effective treatment
High groundwater conditions can lead to:
  System failure (submerged drainfields)
  Reduced treatment efficiency (loss of purification)
Sea level rise further reduces separation over time, increasing vulnerability
Source: Miami-Dade County Plan of Action Report, December 2020 (modified by Ardurra)
4

## Slide 5: Extensive sampling (‘Grabs’)
13-15 stations, ebb tide sampling
Year 1: 11/20 – 9/21
Year 2: 5/23 – 5/24
Grab samples (nutrients, salinity, chlorophyll, E. coli, Enterococci and qPCR microbial source tracking assays) and sonde (DO, temp, pH, salinity) measurements at all stations
3 wet & 2 dry also w/metals & wastewater tracers
Grabs
2) Total nitrogen and phosphorus
Autosampling at 4 stations
Autosampler
CG city boundary
Grab sampling locations Sonde or buoy location
Autosampler locations
CGW AD
CGW KB
Sonde
Intensive sampling (‘Continuous)
1) Chlorophyll and dissolved oxygen, ETC
Mooring network deployed at least 6 locations
5 from U Mass; and in-kind contributions from FIU

## Slide 6: Sample results – YEAR 1
Red dashed line indicates the regulatory water quality criteria of a geomean of 35 cfu/100mL live enterococci from multiple samples collected within 5 days.
Blue dotted line indicates the EPA recommended Single Sample Threshold of 70 cfu/100mL live enterococci for a “Beach Action Value”
(BAV) decision that triggers swim advisories or warnings due to potential bacterial hazard.
“TNTC” indicates plate counts that are “Too Numerous To Count”, defined as greater than 350 cfu/100mL.
downstream
Live Enterococci Fecal Indicator Bacteria by Site and Date
upstream
Coral Gables Waterway - Surface Sampling Sites
CG-1
CG-2
CG-3
CG-4
CG-5
CG-6
CG-7
CG-8
CG-8a1
CG-8a2
CG-8b
CG-9
CG-10
CG-10a
CG-11
CG-12
CG-13
Live enterococci CFU/100mL
80
60
40
20
0
360
340
320
300
280
260
240
220
200
180
160
140
120
100
9/29/20
10/14/20
10/28/20
11/12/20
12/14/20
01/27/21
02/25/21
03/25/21
04/23/21
05/24/21
06/07/21
06/23/21
07/21/21
08/05/21
08/19/21
09/03/21
TNTC TNTC
TNTC TNTC
TNTC TNTC
TNTC
Snapper Creek

## Slide 7: Sample results – YEAR 2
Red line indicates the Quantitative Microbial Risk Assessment (QMRA) suggested risk-based threshold (RBT) for exposure to recreational water contaminated with sewage of uncertain age (525 copies of HF183 per 100 mL of water).
Sources near outfalls had the highest exposure levels (pump south of Biltmore and Riviera Dr. outfall), followed by a US1 site, but most sites showed some evidence of human-source bacteria
Microbial Source Tracking for different potential sources of fecal indicator bacteria from dog and bird did not show much exposure risk due to these sources
Gidley & Sinigalliano NOAA/UM

## Slide 8: Travel Times & Water Quality Indicators from Septic Systems
Parameter | Parameter Limit (mg/l) | Average (mg/l) | Max (mg/l)
Nitrogen (TN) | 0.31 | 0.9 | 1.5
Phosphorus (TP) | 0.007 | 0.04 | 0.07
Sucralose | N/A | 453 | 1135
Nitrogen (TN)
Phosphorus (TP)
Contaminant Travel:
Up to ~1,900 ft in 1 year
1–2 yrs: localized impact
3–5 yrs: expanded plume
Water Quality Findings:
Nitrogen (TN) and Phosphorus (TP) exceed regulatory limits
Sucralose is a wastewater tracer that indicates human effluent presence.
Sucralose detected → indicates
wastewater influence

## Slide 9: Program Purpose
Protect Water Quality
Reduce nutrient and pathogen loading
Protect Biscayne Bay and local waterways
Improve groundwater quality
Modernize Infrastructure
Address aging and failing septic systems
Improve long-term wastewater reliability
Plan a transition toward centralized sewer service
Plan for the Future
Provide a roadmap for phased implementation
Position the City for long-term resilience
Incorporate sea level rise and groundwater considerations
Current Situation:
~50% of City (~7,655 properties) served by septic systems
Many systems do not meet modern standards
9

## Slide 10: Program Benefits
Program Benefits
No future maintenance costs for property owners or costs to repair/replace septic systems. Centralized city-owned sewer system provides increased reliability.
Enhances property value by removing septic systems.
Reduces pollution discharge into groundwater and waterways, better protecting environmental and human health, including a reduction in frequency of algae blooms and fish kill.
Reduces Maintenance Burden
10
Increases Property Values
Better for Environment & Human Health

## Slide 11: Septic Tanks - Lifespan
Average Septic Tank Lifespan in Florida: Across the United States, most septic tanks are designed to last several decades. The Environmental Protection Agency states that well-maintained septic systems can last 20 to 40 years or more. In Florida, that lifespan depends heavily on tank material and local conditions.
11
Tank Material | Typical Lifespan
Concrete | 30 to 50 years
Fiberglass | 25 to 35 years
Plastic or polyethylene | 20 to 30 years
Drain Field Lifespan Compared to Septic Tanks: Drain fields typically have a shorter lifespan than septic tanks. In Florida, drain fields often last 15 to 30 years, depending on soil, water use, and maintenance. Protecting the drain field is critical. Homeowners should avoid driving or parking vehicles over it, diverting roof and surface water away, and avoid planting trees with aggressive roots nearby.

## Slide 12: Septic Tanks - Lifespan
Factors Impacting How Long a Septic Tanks and Drain Fields Last: Several controllable and uncontrollable factors influence septic tank and drain field lifespan.
12
Tank Material and Build Quality: Not all septic tanks are created equal. Concrete tanks built with proper reinforcement and quality materials last far longer than poorly constructed ones. Low-quality concrete can crack or deteriorate faster when exposed to moisture and soil acidity.
High Water Tables: Many areas of Florida have naturally high-water tables. During rainy seasons, groundwater can rise close to the surface. When soil becomes saturated, wastewater has nowhere to go. This puts pressure on the tank and drain field and can cause backups, slow drainage, and system failure over time.
Heavy Rainfall and Storms – 52 Inches Per Year: Florida receives significantly more rainfall than most states. Miami-Dade County receives approx. 52 inches per year. Prolonged rain can flood drainage fields and reduce the soil’s ability to treat wastewater. Repeated soil saturation and flooding shorten the lifespan of both the tank and the drain field, especially if the system is already aging.
Sandy Soil Conditions, Driveways and Tree Roots: Sandy soil drains quickly, which can be helpful, but it also shifts easily. Soil movement can stress pipes, vehicle pressure, and tree roots can cause small cracks in pipes and concrete tanks and affect how well the drain field distributes water. Improperly installed systems are especially vulnerable.

## Slide 14: Priority Area: City 4 Expansion
14

## Slide 15: Proposed Improvements – City 4 Expansion
15
Scope of Work
Design and construct a gravity sanitary sewer collection system
Includes service lateral line in right-of-way for 1,231 properties
Design and construct new sanitary sewer pump station and force main
Roadway resurfacing
TYPE | QUANTITY | UNIT
Manholes | 267 | EA
Gravity Mains | 73,954 | LF
Force Main | 117 | LF
Pump Station | 1 | EA

## Slide 16: Conceptual Layout-City 4 Expansion
LEGEND
12

## Slide 17: City 4 Exp. – Proposed Pump Station Location
The expansion basin, City 4, will feature its PS located in Ruth Bryan Owen Waterway Park, which is the current location for the existing Basin City 4 PS.

## Slide 18: Priority Area: City 7

## Slide 19: Proposed Improvements – City 7
Scope of Work
Design and construct a gravity sanitary sewer collection system
Includes service lateral line in right-of-way for 192 properties
Design and construct new sanitary sewer pump station and force main
Roadway resurfacing
TYPE | QUANTITY | UNIT
Manholes | 45 | EA
Gravity Mains | 13,254 | LF
Force Main | 2,941 | LF
Pump Station | 1 | EA

## Slide 20
Conceptual Layout-City 7 Basin
LEGEND

## Slide 21: City 7 – Pump Station Location
The proposed location is within the ROW owned by the City, situated in a median that primarily consists of green space with some existing trees located by Sevilla Ave. and N. Greenway Dr.

## Slide 22: Priority Area: City 8

## Slide 23: Proposed Improvements – City 8
Scope of Work
Design and construct a gravity sanitary sewer collection system
Includes service lateral line in right-of-way for 159 properties
Design and construct new sanitary sewer pump station and force main
Roadway resurfacing
TYPE | QUANTITY | UNIT
Manholes | 40 | EA
Gravity Mains | 11,944 | LF
Force Main | - | LF
Pump Station | 1 | EA

## Slide 24
Conceptual Layout-City 8 Basin
LEGEND

## Slide 25: City 8 – Pump Station Location
The proposed pump station is located at an existing Private Pump Station (PVT) location and will be rehabilitated.

## Slide 26: Proposed Improvements
Sample Pump Station (PS)
Layout

## Slide 28: Estimated Costs and Funding
City 4 Expansion (New Basin)
Preliminary Rough Order of Magnitude Cost Estimate:
  Total Cost for Basin: $56.3M
  Number of Parcels: 1,231
  Cost per Parcel: $45.7K
* Please note that all estimated costs are based on current dollars and are subject to change due to inflation, material costs, labor rates, and other economic factors. Final costs
may vary depending on the timeline of each project.
* Estimated cost for work in private property: $20,000

## Slide 29: Estimated Costs and Funding
Possible Repayment Options for City 4 Expansion Assessment
Pay upfront – No financing or interest charges – Approximately $45,750
Pay off at any time – Incur financing cost but only incur interest charges up
to the time of pay off
Pay over life of loan – Incur financing and interest costs each year (estimate):
o 5 year - 4.25% Int. $10,350 per year
o 7 year - 4.50% Int. $7,775 per year
o 10 year - 4.75% Int. $5,850 per year
o 20 year - 5.25% Int. $3,750 per year *
o 30 year - 5.75% Int. $3,235 per year *
Note: Interest rates listed above are for illustrative purposes only and should not be relied on. They are subject to change based on market conditions at the time the loan/bonds are issued.
*Part of a Miami-Dade County Special Benefit Area.

## Slide 30: Estimated Costs and Funding
City 7 (New Basin)
Preliminary Rough Order of Magnitude Cost Estimate:
  Total Cost for Basin: $10M
  Number of Parcels: 192
  Cost per Parcel: $52K
City 8 (New Basin)
Preliminary Rough Order of Magnitude Cost Estimate:
  Total Cost for Basin: $7M
  Number of Parcels: 159
  Cost per Parcel: $44K
* Please note that all estimated costs are based on current dollars and are subject to change due to inflation, material costs, labor rates, and other economic factors. Final costs
may vary depending on the timeline of each project.
* Estimated cost for work in private property: $20,000

## Slide 31: Estimated Costs and Funding
Possible Repayment Options for City 7 Assessment
    Pay upfront – No financing or interest charges – Approximately $52,000
    Pay off at any time – Incur financing cost but only incur interest charges up to the time of pay off
    Pay over life of loan – Incur financing and interest costs each year (estimate):
  5 year - 4.25% Int. $11,765 per year
  7 year - 4.50% Int. $8,825 per year
  10 year - 4.75% Int. $6,655 per year
  20 year - 5.25% Int. $4,265 per year *
  30 year – 5.75% Int. $3,680 per year *
Note: Interest rates listed above are for illustrative purposes only and should not be relied on. They are subject to change based on market conditions at the time the loan/bonds are issued.
*Part of a Miami-Dade County Special Benefit Area.

## Slide 32: Estimated Costs and Funding
Possible Repayment Options for City 8 Assessment
    Pay upfront – No financing or interest charges – Approximately $44,000
    Pay off at any time – Incur financing cost but only incur interest charges up to the time of pay off
    Pay over life of loan – Incur financing and interest costs each year (estimate):
  5 year - 4.25% Int. $9,955 per year
  7 year - 4.50% Int. $7,470 per year
  10 year - 4.75% Int. $5,630 per year
  20 year - 5.25% Int. $3,605 per year *
  30 year - 5.75% Int. $3,115 per year *
  Note: Interest rates listed above are for illustrative purposes only and should not be relied on. They are subject to change based on market conditions at the time the loan/bonds are issued.
  *Part of a Miami-Dade County Special Benefit Area.

## Slide 33: Resources for Homeowners
Miami-Dade County Septic System Care:
  Provides homeowner guidance on septic system maintenance and best practices.
  www.miamidade.gov/global/economy/environm ent/septic-system-care.page
Miami Waterkeeper:
  Highlights the impact of septic failures on water quality and promotes sustainable wastewater solutions through advocacy and education.
  www.miamiwaterkeeper.org/septic

## Slide 34: Informational Public Meeting #2 City 4 Expansion, City 7 & 8 Basins
24

## Slide 36
For Additional Information, Visit:
  https://www.coralgables.com/septic-sewer-conversion-program
Find Your Basin:
  https://king.maps.arcgis.com/apps/instant/lookup/index.html?appid=989d1bf2f3464de6b4340e416d742c6d
Complete Sewer Assessment Survey:
https://survey123.arcgis.com/share/0b137a291dc744d7b8a89f8f72b6aad6